## Slide 1
Pre-Workshop Setup
Download Presentation
Go to below URL and download pdf/ppt file
  https://goo.gl/p3Su87
Connect to Board
Power on Beaglebone Black Wireless
Plug in USB Cable to computer
Plug in USB cable to BBW
After ~4 minutes connect to board’s wifi access point
  ssid is what you see on the board’s label
  Passcode is beaglebone_<what you see on the label>
Plug in Beaglebone Black Wireless

## Slide 2: Super Intro Embedded Linux Workshop

## Slide 3
Goals
Learn to use Beaglebone Black wireless
Play BopIt Game (using Computer Mouse)
Learn how to control peripherals via Python
Play BopIt Game (using Beaglebone Sensors)

## Slide 4
Python
If your not family with Python
  Ask a neighbor
  Use a search engine
  Quickly look at: http://www.nerdparadise.com/programming/python4minutes

## Slide 5
Beaglebone Black
Open Source Community Board
Uses Cortex A8 MPU
Runs at 1 GHz max
Supports ALOT of peripherals that are accessible

## Slide 6
Lets Get Started

## Slide 7
Pre-Workshop Setup
Download Presentation
Go to below URL and download pdf/ppt file
  https://goo.gl/p3Su87
Connect to Board
Power on Beaglebone Black Wireless
Plug in USB Cable to computer
Plug in USB cable to BBW
After ~4 minutes connect to board’s wifi access point
  ssid is what you see on the board’s label
  Passcode is beaglebone_<what you see on the label>
Plug in Beaglebone Black Wireless

## Slide 8
Beaglebone Workshop Cape

## Slide 9
Cloud 9
Browser Base IDE (Supports Python and other languages)
When Beaglebone Black is connected to PC and booted Cloud 9 can be accessed by going to:
  192.168.7.2:3000 (Windows)
  192.168.6.2:3000 (Linux/Mac)

## Slide 10
Cloud 9 Screen

## Slide 11
Create New File
Create New File
  Goto File->New File
Now Save File
  Goto File->Save
  Give file a name but it MUST end with .py
  Hit green Save button

## Slide 12
Run Program
Always save File before running
  Either File->Save or Ctrl and S (at the same time)
Two ways to run program (after saving)
  Hit Green Run Button
  Go to the “bash - “beaglebone” window
    Type python “<your full filename>”
    To halt execution hit Ctrl and C (and hold it)

## Slide 13
Running via Command Line

## Slide 14
Final Cool Project

## Slide 15
Beaglebone Based Bop It
Create a simplified version of the game Bop It

## Slide 16
Peripheral - GPIO
Input -
  High (1) : voltage >= 2 V
  Low (0) : voltage <= .8 V
Output
  High (1) : 3.3 V
  Low (0) : 0 V

## Slide 17
Component Push Button
Basic Switch – by default pins 1 and 2 are not connected to pins 3 and 4.

## Slide 18
Schematic - Push Button
BBB Header Pin P8_10 is connected to one side of tactile switch. Ground is connected to other side of tactile switch.

## Slide 19
Peripheral GPIO - Quiz
What is the value of a input pin when nothing is driving it (outputting a voltage to it)?

## Slide 20
Peripheral GPIO - Quiz
What is the value of a input pin when nothing is driving it (outputting a voltage to it)?
          NO ONE KNOWS

## Slide 21
Hardware Concept - Pullup and Pulldown
Typical Usage:
  Provide a steady/default value
BBB Pin Configuration:
  Supports internal pullup and internal pulldown
  Adafruit library by default configures GPIOs to be pull ups

## Slide 22
Adafruit Library – 1 Sec Introduction
Adafruit created a peripheral library for BBB:
  Python Based
  Simple to Use
  Lose some flexibility

## Slide 23
Adafruit Library – GPIO Class
Including/Import
  import Adafruit_BBIO.GPIO as GPIO
Configuration:
  Input
    GPIO.setup(“<PIN_NAME>”, GPIO.IN)
  Output
    GPIO.setup(“<PIN_NAME>”, GPIO.OUT)
Usage:
  Input
    GPIO.input(“<PIN_NAME>”)
      Returns 1/True if voltage is high and returns 0/False if voltage is low
    Output
      GPIO.output(“<PIN_NAME>”, GPIO.HIGH) – Output High
      GPIO.output(“<PIN_NAME>”, GPIO.LOW) – Output Low

## Slide 24
Task 1 - GPIO
Create a Python program that outputs (via 'print' statement) some phrase when the push button goes low
Remember:
Try:
Tap push button once as fast as possible and see what your program outputs

## Slide 25
Task 1 - Solution

## Slide 26
GPIO (Debounce)
Switch Bouncing:
  Occurs when pushing or release buttons/switch

## Slide 27
GPIO Debounce - Solutions
Simple software solution:
  When state change ignore any future state changes for X ms
  Can get complicated.
  Adafruit has another approach that will be discussed later

## Slide 28
Component - Vibration Switch
Slow Vibration Sensor Switch
How does it work:
  1 pin of the switch is connected to a metal pole. Other pin is connected to metal coil that goes around the metal pole.
  Movement = temporary contact

## Slide 29
Adafruit – GPIO Continued
GPIO.wait_for_edge(“<PIN_NAME>”, GPIO.RISING)
  Blocking call
GPIO.add_event_detect(“<PIN_NAME>”, GPIO.FALLING)
  Setup non blocking call
GPIO.event_detected(“<PIN_NAME>”)
  Detect if state transition has occurred

## Slide 30
Peripheral – GPIO (Rising/Falling Edge)
Indicates a transition from a high level to low or vice a versa

## Slide 31
Task 2 – GPIO Event
Similar to previous assignment:
  Output statement when vibration sensor is flicked (NOT TOO HARD)
  Use GPIO event instead of raw input value
Important Hint:
  Make sure in the code you use “P8_8” to refer to the pin. DO NOT use “P8_08”
Question:
To accomplish this assignment would you use falling or rising edge?

## Slide 32
Task 2 - Solution

## Slide 33
Component - Potentiometer
What is it:
  Variable Resistor
  Increase/decrease resistance via knob
  Can be used as a voltage divider
    Middle pin is output of divider

## Slide 34
Peripheral - ADC
Purpose
  Converts analog voltage to digital value
  Useful for sensors that output voltage only
Beaglebone Black's ADC is a 12 bit ADC:
  Digital Value Range
    0 – 4095
  Max support input voltage:
    1.8 V

## Slide 35
Adafruit - ADC
Import:
  import Adafruit_BBIO.ADC as ADC
Configuration:
  ADC.setup()
Reading:
  Value from 0.0 to 1.0
    value = ADC.read(“<PIN_NAME>”)
  Raw Digital Value
    value = ADC.read_raw(“<PIN_NAME>”)

## Slide 36
Task 3
Output message every time push button is pressed
How can I convert the ADC value read in by the Adafruit library and convert it to a voltage?

## Slide 37
Task 3 - Solution

## Slide 38
Peripheral - I2C
Quick Summary
  Uses 2 Pins
    SCL – Clock
    SDA – Data
  Half Duplex
  Speed “Typical” Ranges 1K to 400K
  Supports Multiple Nodes
  Communicate to specific node via unique address
  Multi Master

## Slide 39
Peripheral – I2C (Bus)
Our Friend Pullups are back!

## Slide 40
Peripheral – I2C (Reading/Writing)
Reading Procedure:
  Send node address
  Also set flag to read
  Send address you want to read from
  Read from node
Writing Procedure:
  Send node address
  Also set flag to write
  Send address you want to write to
  Write value(s) to node

## Slide 41
Component – Light Intensity Sensor
Summary:
  Default address 0x39
    Some boards have 49
    marked on then if so use
    0x49 instead
  Requires Configuration
  Has defined sample rate
  Returns ambient light
  levels

## Slide 42
Task 4 – Read Light Sensor
Go To:
https://learn.adafruit.com/setting-up-io-python-library-on-beaglebone-black/i2c
Create program that does the following:
  Configure I2C for slave address 0x39
  Power On Device
    Write value 0x3 to register 0x80 (128 in decimal)
  Wait 14 ms
  In an infinite while loop
    Read and print unsigned 16 bits of data when pushed button is pressed
      From register 0xAC (172 decimal)
Use slave address 0x49 if you see
the following ->
Question:
How does the output change when you block light from it?

## Slide 43
Task 4 - Solutions

## Slide 44
Link to Project
https://www.hackster.io/fcooper27/intro-embedded-linux-06c3b8

## Slide 45
Final Task – Bop It
Create a simplified version of the game Bop It

## Slide 46
Bop It – How It Works
Its a game similar to Simon Says
The game continuously randomly ask the user to perform an action
  Make sure “only” the correct action is performed in X amount of seconds
  Otherwise user loses
Our actions are:
  Turn it – Turn Potentiometer
  Block It – cover light sensor
  Flick it – Flick vibration sensor (NOT TOO HARD)
  Push It – Push tactile button

## Slide 47
Bop It – High Level
Program Starts
Wait 4 seconds and play intro audio
Wait until has pushed and released button (rising edge) the button
Randomly output an action to perform
  Play audio for “correct action”
  Check all actions to see if they are being performed
  Avoid blocking calls.

## Slide 48
Bop It – Python Useful New Functions
Useful new Python Functions:
Sleeping – Block Execution for X amount of seconds. Supports fractional sleep (ms sleep)
  from time import sleep
  sleep(.1) # 100 ms
random.randint(startNum, endNum) – Return random interger between and including startNum and endNum
Find difference in time (ms)
  Call and store
    int(round(time.time() * 1000))
  At a later point call and store
    int(round(time.time() * 1000))
  Take the difference and thats the time difference in ms

## Slide 49
Bop It – PyGame Library
PyGame useful library for making Python games.
https://www.pygame.org/docs/ref/music.html
We will just use audio library
Import:
  from pygame import mixer
Configuration
  mixer.init()
Load Audio File
  sound = mixer.Sound(“<path and name of audio file to load>”)
Play Audio File
  sound.play()
  sound.play(loops=-1)
Stop Playing Audio
  sound.stop()
Check if Audio is playing
  sound.get_busy()

## Slide 50
Bop It – Useful Peripheral Tips
For Turning Detection Function:
  Read ADC, store the time and value read
  Future calls if it was within X amount of sec/ms of the above
    Return false - if the difference between stored and current ADC value is below some threshold
    Return true - if the difference between stored and current ADC value is above some threshold

## Slide 51
Bop It – Useful Peripheral Tips Cont
For Flicking Detection Function:
  Debouncing is very much an issue. So use GPIO event detect.
For Blocking Detection Function
  If light intensity is below a threshold (pick a value via testing) then return true that its currently being blocked otherwise return false
  Remember between each read light intensity calls you need to wait atleast 14 ms.