## Slide 1
Pre-Workshop Setup
Power On Beaglebone Black Wireless
Connect USB cable to board
Connect other end of USB cable to PC
Download Presentation, files and Read Python Tutorial
Go to https://goo.gl/p3Su87
Download presentation (pptx/pdf)
Download bopit.zip and extract bopit.zip
Read the the 4 minute python pdf if you don’t know
python
Connect to Beaglebone Black Wireless access point
Wait ~4 minutes after your board has been powered on
Connect to board’s wifi access point
  Wifi ssid is what you see on the board’s label as “ssid:”
Passcode is beaglebone_ then add what you see on the label.
For the above image the password would be “beaglebone_jkr”

## Slide 2
2
Franklin Cooper
University Marketing Manager
Super Introduction to Embedded Linux Workshop

## Slide 3
Goals
Learn to use Beaglebone Black wireless
Play BopIt Game (using Computer Mouse)
Learn how to control peripherals via Python
Play BopIt Game (using Beaglebone Sensors)

## Slide 4
Python
If your not family with Python
  Ask a neighbor
  Use a search engine
  Quickly look at: https://goo.gl/SnbG6M

## Slide 5
Beaglebone Black Wireless Quick Summary
Open Source Community Board
Uses Cortex A8 MPU
Runs at 1 GHz max
Access to 81 pins ie you can access a lot of peripherals
Integrated Wifi
Intergrated Bluetooth
5

## Slide 6
Beaglebone Workshop Cape
6
Potentiometer
Push Button
Light Sensor
LED
Connected to:
P9_36
Connected to:
P9_19
P9_20
Connected to:
P9_29
Connected to:
P9_46

## Slide 7
Lets Get Started

## Slide 8
Cloud 9 – Quick Summary
8
Browser Base IDE
Supported Languages:
Python
C
C++
and much more
Supports Debugging

## Slide 9
Task 1 – Connect to Cloud 9 IDE
Make sure your connected to your device’s wireless access point
  If not see the first slide for instructions
Open up a web browser (don’t use IE)
  Go to http://192.168.7.2:3000/ (May take 2-3 minutes for page to load)
  You should see something like the below
9

## Slide 10
Cloud 9 – How to Create a New File
10
Create New File
Goto File->New File
Now Save File
Goto File->Save
Give file a name
  MUST end with .py for Python programs
Hit green Save button
Shortcut to Save File
CTRL+S

## Slide 11
Cloud 9 – How to Import a File on Your PC
11
Upload Local File(s)
Goto File->Upload Local Files
Hit “Select files’
Navigate to the files you want to upload
Highlight all the files you want to upload
Hit Open

## Slide 12
Task 2 – Import Workshop Files
12
Upload Local File(s)
Goto File->Upload Local Files
Hit “Select files’
Navigate to where you extracted bopit.zip
Go into the files directory
Highlight all Python files (ends in .py)
Hit Open

## Slide 13
Cloud 9 – Running Program
Hit Run Button to “run your program”
* Important Tip*
Before running save your file first.
13

## Slide 14
Task 3 – Run Bopit_board_test.py Program
Run the bopit_board_test.py program.
This will help verify your board is in working order.
Look at the console and follow the commands.
If you get any failures then alert your instructor.
14

## Slide 15
Play Beaglebone Based Bop It
Goal :
Play Bop It using Push Button, Potentiometer and Light Sensor

## Slide 16
Task 4 – Play TI Beaglebone BopIt
Goto: http://192.168.7.2:8080/workshop/bopit/
Turn down your computer’s speaker (IMPORTANT)
Hit Start
You will see and/or hear a command
Hit the correct button below that corresponds with the command
16

## Slide 17
Hardware – Pinmux
Pinmuxing is when a signal can be connected via a mux (switch) to various other signals
Pinmuxing is used on almost every signal pin on the Beaglebone
Internal
(Inside Chip)
gpio
i2c_sda
External
(What you can access)
P9_29

## Slide 18
Software – Pinmux
To simplify configure a pin’s pinmuxing you can use a program/script called config-pin
debian@beaglebone:~$ config-pin P9_14 pwm
debian@beaglebone:~$ config-pin -q P9_14
P9_14 Mode: pwm
debian@beaglebone:~$ config-pin -l P9_14
default gpio gpio_pu gpio_pd pwm
Output ->
Output ->
Set P9_14 to PWM
Get information regarding
P9_14 current setting
Get list of modes you can
Set P9_14 to
Python version (What you will be using)
workshop.setPinMux("P9_29","gpio")
Set P9_29 to gpio mode.
Modes you will use in this workshop:
gpio and i2c

## Slide 19
Peripheral – GPIO: Basic Electrical Information
19
Input -
  High (1) : voltage >= 2 V
  Low (0) : voltage <= .8 V
Output
  High (1) : 3.3 V
  Low (0) : 0 V

## Slide 20
Hardware - Push Button: Introduction
20
Basic Switch – by default pins 1 and 2 are not connected to pins 3 and 4.

## Slide 21
Hardware – Push Button: Wiring
21
BBB Header Pin P9_29 is connected to one side of tactile switch. VCC is connected to other side of tactile switch.
P9_29
+3.3V

## Slide 22
Quiz 1 - GPIO
22
What is the value of a input pin when nothing is driving it (outputting a voltage to it)?

## Slide 23
Quiz 1 - GPIO
23
What is the value of a input pin when nothing is driving it (outputting a voltage to it)?
NO ONE KNOWS

## Slide 24
Hardware – Pullup and Pull Down Resistors
24
Typical Usage:
  Provide a steady/default value
BBB Pin Configuration:
  Supports internal pullup and internal pulldown
  Adafruit library allows you to configure internal pull up and pull down
P9_29
+3.3V

## Slide 25
Adafruit Library – Quick Introduction
Adafruit created a peripheral library for BBB:
  Python Based
  Simple to Use
  Lose some flexibility
25

## Slide 26
Adafruit Library – GPIO (Input)
26
Including/Import
import Adafruit_BBIO.GPIO as GPIO
What does this mean?

## Slide 27
Adafruit Library – GPIO (Input)
27
Including/Import
import Adafruit_BBIO.GPIO as GPIO
Library alias (reduce the amount of typing you do)

## Slide 28
Adafruit Library – GPIO (Input)
28
Including/Import
import Adafruit_BBIO.GPIO as GPIO
Configuration:
GPIO.setup(“<PIN_NAME>”, GPIO.IN)
Configures GPIO as an input (pull up resistor by default)
GPIO.setup(“<PIN_NAME>”, GPIO.IN, pull_up_down=GPIO.PUD_DOWN)
Configures GPIO as an input (pull down by default)
Usage:
GPIO.input(“<PIN_NAME>”)
Returns 1/True if voltage is high and returns 0/False if voltage is low

## Slide 29
Adafruit Library – GPIO (Output)
29
Including/Import
import Adafruit_BBIO.GPIO as GPIO
Configuration:
GPIO.setup(“<PIN_NAME>”, GPIO.OUT)
Configure pin as an output
Usage:
GPIO.output(“<PIN_NAME>”, GPIO.HIGH)
Set pin to high
GPIO.output(“<PIN_NAME>”, GPIO.LOW)
Set pin to low

## Slide 30
Task 5 – Basic GPIO Program
30
Goal: print a message every time you push the button
Open gpio_input.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember:
Try:
Tap push button once as fast as possible and see what your program outputs
P9_29
+3.3V
Configure internally

## Slide 31
Before you start coding
31
The solutions to each task is located in the folder solution.
However, avoid peeking at the answer unless you stuck and have no way to figure things out.
Most problems you may have is likely python syntax issues. So feel free to use your partner’s computer or phone to look up what your error means and how to fix it.
Also look at 4 Minute Python Crash Course _ Nerd Paradise.pdf included in the zip file to learn everything you need to know for this workshop.
The code you will type is usually no more than 5 lines.

## Slide 32
Task 5 – Basic GPIO Program (Solution)
32

## Slide 33
Hardware - Issue
33
Switch Bouncing:
  Occurs when pushing or release buttons/switch
How do you solve it?

## Slide 34
Hardware – Debounce Solution
34
Simple software solution:
  When state change ignore any future state changes for X ms
Detect button press
Detect button release
Don’t read for X ms
Don’t read for X ms

## Slide 35
Task 6 – Debounce GPIO Program
35
Goal: print a message ONCE (ie debounce) every time you push the button
Open gpio_input_debounce.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember:
Try:
Feel free to change the debounce timeout value to see how it impacts the program
P9_29
+3.3V
Configure internally

## Slide 36
Task 6 – Debounce GPIO Program Solution
36

## Slide 37
Task 7 – Update Bopit to use Push Button
If bopit.py is running make sure you stop it.
Open bopit.py file that you previously loaded into Cloud 9.
Replace all the lines that says “## PUT YOUR CODE HERE ##” within the functions “gpioSetup()” and getPushButtonVal()”.
Read the comment to understand what your being asked to do for the lines your writing code for. Your pretty much taking the code you wrote before and adding it here.
Run bopit.py program
Go to http://192.168.7.2:8080/workshop/bopit/
If things are working properly every time it says push it you can use the push button the Beaglebone
37

## Slide 38
Hardware: Potentiometer
38
What is it:
  Variable Resistor
  Increase/decrease resistance via knob
  Can be used as a voltage divider
    Middle pin is output of divider

## Slide 39
Peripheral – Analog to Digital Converter (ADC)
39
Purpose
  Converts analog voltage to digital value
  Useful for sensors that output voltage only
Beaglebone Black's ADC is a 12 bit ADC:
  Digital Value Range
    0 – 4095
  Max support input voltage:
    1.8 V

## Slide 40
Adafruit Library – ADC
40
Including/Import
import Adafruit_BBIO.ADC as ADC
Configuration:
ADC.setup()
Usage:
ADC.read(“<PIN_NAME>”)
Returns a decimal value from 0.0 – 1.0
ADC.read_raw(“<PIN_NAME>”)
Returns a digital value from 0 - 4095

## Slide 41
Task 8 – Read Potentiometer
Goal: Print the voltage being read by the potentiometer
Open adc.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember:
P9_36

## Slide 42
Task 8 – Read Potentiometer Solution
42

## Slide 43
Task 9 – Update Bopit to use Potentiometer
If bopit.py is running make sure you stop it.
Open bopit.py file that you previously loaded into Cloud 9.
Replace all the lines that says “## PUT YOUR CODE HERE ##” within “adcSetup()” and “readPotentiometerVal()” function.
Read the comment to understand what your being asked to do for the lines your writing code for. Your pretty much taking the code you wrote before and adding it here.
Run bopit.py program
Go to http://192.168.7.2:8080/workshop/bopit/
If things are working properly every time it says push it you can use the push button, and when it says twist it you can twist the potentiometer (make sure you twist it by a good amount
43

## Slide 44
Peripheral – I2C Quick Summary
44
Quick Summary
  Uses 2 Pins
    SCL – Clock
    SDA – Data
  Half Duplex
  Speed “Typical” Ranges 1K to 400K
  Supports Multiple Nodes
  Communicate to specific node via unique address
  Multi Master

## Slide 45
Hardware – Light Intensity Sensor
45
Summary:
  Default address 0x29
  Requires Configuration
  Has defined sample rate
  Returns ambient light
  levels

## Slide 46
Task 10 – I2C Light Intensity
Goal: print light intensity every second
Open i2c.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Update the code based on the comments that explain what is expected.
Use the information I provided in the previous slides to do this as well as the smbus pdf included in the bopit.zip you extracted earlier.
Run the program and tap the button quickly to see if you achieve your goal
Remember/Hint:
  Device is on bus 2 (not 0 which the pdf uses)
  Device address is 0x29
Try:
Feel free to change the debounce timeout value to see how it impacts the program

## Slide 47
Task 10 – I2C Light Intensity Solution

## Slide 48
Task 11 – Update Bopit to use Light Sensor
If bopit.py is running make sure you stop it.
Open bopit.py file that you previously loaded into Cloud 9.
Replace all the lines that says “## PUT YOUR CODE HERE ##” with your code within functions “i2cSetup()” and “getLightValue()”.
Read the comment to understand what your being asked to do for the lines your writing code for. Your pretty much taking the code you wrote before and adding it here.
Run bopit.py program
Go to http://192.168.7.2:8080/workshop/bopit/
If things are working properly every time it says push it you can use the push button, when it says twist it you can twist the potentiometer (make sure you twist it by a good amount and when it says block it you put your hand over the light sensor.
48