## Slide 1
Pre-Workshop Setup
Power On Beaglebone Black Wireless
Connect USB cable to board
Connect other end of USB cable to PC
Download Presentation, files and Read Python Tutorial
Go to https://goo.gl/p3Su87
Download presentation (pptx/pdf)
Download bopit.zip and extract bopit.zip
Read https://goo.gl/SnbG6M
Connect to Beaglebone Black Wireless access point
Wait ~4 minutes after your board has been powered on
Connect to board’s wifi access point
  ssid is what you see on the board’s label
  Passcode is beaglebone_ then add what you see on the label

## Slide 2: Super Introduction to Embedded Linux Workshop
Franklin Cooper
University Marketing Manager

## Slide 3
Goals
Learn to use Beaglebone Black wireless
Play BopIt Game (using Computer Mouse)
Learn how to control peripherals via Python
Play BopIt Game (using Beaglebone Sensors)

## Slide 4
Python
If your not family with Python
  Ask a neighbor
  Use a search engine
  Quickly look at: https://goo.gl/SnbG6M

## Slide 5: Beaglebone Black Wireless Quick Summary
Open Source Community Board
Uses Cortex A8 MPU
Runs at 1 GHz max
Access to 81 pins ie you can access a lot of peripherals
Integrated Wifi
Intergrated Bluetooth

## Slide 6: Beaglebone Workshop Cape
Potentiometer
Push Button
Light Sensor
LED
Connected to:
P9_36
Connected to:
P9_19
P9_20
Connected to:
P9_29
Connected to:
P9_46

## Slide 7
Lets Get Started

## Slide 8: Cloud 9 – Quick Summary
Browser Base IDE
Supported Languages:
Python
C
C++
and much more
Supports Debugging

## Slide 9: Task 1 – Connect to Cloud 9 IDE
Make sure your connected to your device’s wireless access point
  If not see the first slide for instructions
Open up a web browser (don’t use IE)
  Go to http://192.168.7.2:3000/ (May take 2-3 minutes for page to load)
  You should see something like the below

## Slide 10: Cloud 9 – How to Create a New File
Create New File
Goto File->New File
Now Save File
Goto File->Save
Give file a name
  MUST end with .py for Python programs
Hit green Save button
Shortcut to Save File
CTRL+S

## Slide 11: Cloud 9 – How to Import a File on Your PC
Upload Local File(s)
Goto File->Upload Local Files
Hit “Select files’
Navigate to the files you want to upload
Highlight all the files you want to upload
Hit Open

## Slide 12: Task 2 – Import Workshop Files
Upload Local File(s)
Goto File->Upload Local Files
Hit “Select files’
Navigate to where you extracted bopit.zip
Go into the files directory
Highlight all Python files (ends in .py)
Hit Open

## Slide 13: Cloud 9 – Running Program
Hit Run Button to “run your program”
* Important Tip*
Before running save your file first.

## Slide 14: Task 3 – Run Bopit.py Program
Run the bopit.py program.
You should see something similar to the image on the right if it is running properly

## Slide 15
Play Beaglebone Based Bop It
Goal :
Play Bop It using Push Button, Potentiometer and Light Sensor

## Slide 16: Task 4 – Play TI Beaglebone BopIt
Goto: http://192.168.7.2:8080/workshop/bopit/
Turn down your computer’s speaker (IMPORTANT)
Hit Start
You will see and/or hear a command
Hit the correct button below that corresponds with the command

## Slide 17: Hardware – Pinmux
Internal
(Inside Chip)
gpio
i2c_sda
External
(What you can access)
P9_29
Pinmuxing is when a signal can be connected via a mux (switch) to various other signals
Pinmuxing is used on almost every signal pin on the Beaglebone

## Slide 18: Software – Pinmux
To simplify configure a pin’s pinmuxing you can use a program/script called config-pin
debian@beaglebone:~$ config-pin P9_14 pwm
debian@beaglebone:~$ config-pin -q P9_14
P9_14 Mode: pwm
debian@beaglebone:~$ config-pin -l P9_14
default gpio gpio_pu gpio_pd pwm
Output ->
Output ->
Set P9_14 to PWM
Get information regarding
P9_14 current setting
Get list of modes you can
Set P9_14 to
Python version (What you will be using)
workshop.setPinMux("P9_29","gpio")
Set P9_29 to gpio mode.
Modes you will use in this workshop:
gpio and i2c

## Slide 19: Peripheral – GPIO: Basic Electrical Information
Input -
  High (1) : voltage >= 2 V
  Low (0) : voltage <= .8 V
Output
  High (1) : 3.3 V
  Low (0) : 0 V

## Slide 20: Hardware - Push Button: Introduction
Basic Switch – by default pins 1 and 2 are not connected to pins 3 and 4.

## Slide 21: Hardware – Push Button: Wiring
BBB Header Pin P9_29 is connected to one side of tactile switch. VCC is connected to other side of tactile switch.
P9_29
+3.3V

## Slide 22: Quiz 1 - GPIO
What is the value of a input pin when nothing is driving it (outputting a voltage to it)?

## Slide 23: Quiz 1 - GPIO
What is the value of a input pin when nothing is driving it (outputting a voltage to it)?
          NO ONE KNOWS

## Slide 24: Hardware – Pullup and Pull Down Resistors
Typical Usage:
  Provide a steady/default value
BBB Pin Configuration:
  Supports internal pullup and internal pulldown
  Adafruit library allows you to configure internal pull up and pull down
P9_29
+3.3V

## Slide 25: Adafruit Library – Quick Introduction
Adafruit created a peripheral library for BBB:
  Python Based
  Simple to Use
  Lose some flexibility

## Slide 26: Adafruit Library – GPIO (Input)
Including/Import
import Adafruit_BBIO.GPIO as GPIO
Configuration:
GPIO.setup(“<PIN_NAME>”, GPIO.IN)
Configures GPIO as an input (pull up resistor by default)
GPIO.setup(“<PIN_NAME>”, GPIO.IN, pull_up_down=GPIO.PUD_DOWN)
Configures GPIO as an input (pull down by default)
Usage:
GPIO.input(“<PIN_NAME>”)
Returns 1/True if voltage is high and returns 0/False if voltage is low

## Slide 27: Adafruit Library – GPIO (Output)
Including/Import
import Adafruit_BBIO.GPIO as GPIO
Configuration:
GPIO.setup(“<PIN_NAME>”, GPIO.OUT)
Configure pin as an output
Usage:
GPIO.output(“<PIN_NAME>”, GPIO.HIGH)
Set pin to high
GPIO.output(“<PIN_NAME>”, GPIO.LOW)
Set pin to low

## Slide 28: Task 5 – Basic GPIO Program
Goal: print a message every time you push the button
Open gpio_input.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember:
Try:
Tap push button once as fast as possible and see what your program outputs
P9_29
+3.3V
Configure internally

## Slide 29: Task 5 – Basic GPIO Program (Solution)

## Slide 30: Hardware - Debounce
Switch Bouncing:
  Occurs when pushing or release buttons/switch

## Slide 31: Hardware – Debounce Solution
Simple software solution:
  When state change ignore any future state changes for X ms
Detect button press
Detect button release
Don’t read for X ms
Don’t read for X ms

## Slide 32: Task 6 – Debounce GPIO Program
Goal: print a message ONCE (ie debounce) every time you push the button
Open gpio_input_debounce.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember:
Try:
Feel free to change the debounce timeout value to see how it impacts the program
P9_29
+3.3V
Configure internally

## Slide 33: Task 6 – Debounce GPIO Program Solution

## Slide 34: Task 6 – Update Bopit to use Push Button
If bopit.py is running make sure you stop it.
Open bopit.py file that you previously loaded into Cloud 9.
Replace all the lines that says “## PUT YOUR CODE HERE ##” with your code. But only sections that says “# GPIO Code below” right above it
Read the comment to understand what your being asked to do for the lines your writing code for. Your pretty much taking the code you wrote before and adding it here.
Run bopit.py program
Go to http://192.168.7.2:8080/workshop/bopit/
If things are working properly every time it says push it you can use the push button the Beaglebone

## Slide 35: Hardware: Potentiometer
What is it:
  Variable Resistor
  Increase/decrease resistance via knob
  Can be used as a voltage divider
    Middle pin is output of divider

## Slide 36: Peripheral – Analog to Digital Converter (ADC)
Purpose
  Converts analog voltage to digital value
  Useful for sensors that output voltage only
Beaglebone Black's ADC is a 12 bit ADC:
  Digital Value Range
    0 – 4095
  Max support input voltage:
    1.8 V

## Slide 37: Adafruit Library – ADC
Including/Import
  import Adafruit_BBIO.ADC as ADC
Configuration:
ADC.setup()
Usage:
ADC.read(“<PIN_NAME>”)
Returns a decimal value from 0.0 – 1.0
ADC.read_raw(“<PIN_NAME>”)
  Returns a digital value from 0 - 4095

## Slide 38: Task 7 – Read Potentiometer
Goal: Print the voltage being read by the potentiometer
Open adc.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember:
P9_36

## Slide 39: Task 7 – Read Potentiometer Solution

## Slide 40: Task 8 – Update Bopit to use Potentiometer
If bopit.py is running make sure you stop it.
Open bopit.py file that you previously loaded into Cloud 9.
Replace all the lines that says “## PUT YOUR CODE HERE ##” with your code. But only sections that says “# ADC Code below” right above it
Read the comment to understand what your being asked to do for the lines your writing code for. Your pretty much taking the code you wrote before and adding it here.
Run bopit.py program
Go to http://192.168.7.2:8080/workshop/bopit/
If things are working properly every time it says push it you can use the push button, and when it says twist it you can twist the potentiometer (make sure you twist it by a good amount

## Slide 41: Peripheral – I2C Quick Summary
Quick Summary
  Uses 2 Pins
    SCL – Clock
    SDA – Data
  Half Duplex
  Speed “Typical” Ranges 1K to 400K
  Supports Multiple Nodes
  Communicate to specific node via unique address
  Multi Master

## Slide 42: Hardware – Light Intensity Sensor
Summary:
  Default address 0x29
  Requires Configuration
  Has defined sample rate
  Returns ambient light
  levels

## Slide 43: Task 9 – I2C Light Intensity
Goal: print light intensity every second
Open i2c.py file that you previously loaded into Cloud 9.
Replace all the lines that says ## PUT YOUR CODE HERE ## with your code
Read the comment to understand what your being asked to do for the lines your writing code for
Use the information I provided in the previous slides to do this
Run the program and tap the button quickly to see if you achieve your goal
Remember/Hint:
  Device is on bus 2
  Device address is 0x29
Try:
Feel free to change the debounce timeout value to see how it impacts the program

## Slide 44: Task 9 – I2C Light Intensity Solution

## Slide 45: Task 10 – Update Bopit to use Light Sensor
If bopit.py is running make sure you stop it.
Open bopit.py file that you previously loaded into Cloud 9.
Replace all the lines that says “## PUT YOUR CODE HERE ##” with your code. But only sections that says “# I2C Code below” right above it
Read the comment to understand what your being asked to do for the lines your writing code for. Your pretty much taking the code you wrote before and adding it here.
Run bopit.py program
Go to http://192.168.7.2:8080/workshop/bopit/
If things are working properly every time it says push it you can use the push button, when it says twist it you can twist the potentiometer (make sure you twist it by a good amount and when it says block it you put your hand over the light sensor.